## Slide 1: Let’s Chat About OSC
Hans Hinrichsen

## Slide 2: What is OSC
Flexible and customizable protocol – used in music, theatre, and live event applications
Designed as the replacement to MIDI using networking technology
Simple to understand
Very powerful and expandable
Let’s look at OSCWidgets!

## Slide 3: What makes an OSC command?
An OSC Pattern followed by zero or more arguments
Patterns are defined by the control software you are working with
  Eos: /eos/cue/1/fire
  ColorSource: /cs/playback/go
  Hog: /hog/playback/go/0
  QLab: /workspace/1/go

## Slide 4: OSC Arguments
Arguments are extra pieces of data sent with a Pattern
There can be many types – the controller you use will tell you what types to send
The standard defines:
  Integer (…-2, -1, 0, 1, 2, 3, ….)
  Floating point number (1.0001, -9.889, etc…)
  OSC-Timetag (number of fractional seconds since January 1, 1900)
  OSC-String (“Hello world!”)
  OSC-blob (binary data)

## Slide 5: What makes an OSC argument?
Here are some example arguments for real-world patterns
  Eos:
    Command: /eos/cue/fire
    Argument: 1
    Result: Run cue 1
  ColorSource:
    Command: /cs/playback
    Arguments: 12, “fire”, 1
    Result: Pressed the bump button DOWN for playback 12
  Hog:
    Command: /hog/hardware/fader/0
    Argument: 127
    Result: Sets the Hog 4 Grand Master to 50% (0-255 range)

## Slide 6: OSC Messages
Entering arguments in software will vary based on the platform used to send them!
TouchOSC
Eos Magic Sheets
OSCWidgets

## Slide 7: How do I know what commands are supported?
Check the user manuals and/or online help pages
Eos: http://www.etcconnect.com/webdocs/Controls/EosFamilyOnlineHelp/Default.htm
Hog: https://www.highend.com/pub/support/controllers/documents/HTML/en/sect-osc_mappings.htm
ColorSource AV User Manual: http://www.etcconnect.com/WorkArea/DownloadAsset.aspx?id=10737495606
QLab: https://figure53.com/docs/qlab/v3/scripting/osc-dictionary-v3/

## Slide 8: Connecting devices
OSC is transport-independent protocol
A few ETC has used:
  UDP
  TCP/IP – packet length headers
  TCP/IP – SLIP
  USB/Serial
Let’s talk details about IP-based…

## Slide 9: OSC – UDP vs TCP
IP: UDP vs TCP
  User Datagram Protocol
    Stateless – no “connection”
    Does not guarantee message reaches destination
  Transmission Control Protocol
    Direct connection
    Guaranteed delivery
    Two OSC versions – 1.0 (packet length) and 1.1 (SLIP)
      Must match for two devices to talk to each other!
IP: Ports
  An endpoint or “mailbox” associated with an IP address
  10.101.2.177:53000

## Slide 10: Choosing Ports
TCP
  TCP ports are typically hard-coded and listed in documentation
  Usually a single TCP port is available
  Each device has a unique connection to the controller
  Controller can respond directly to a device
UDP
  UDP ports are typically configured
  The Receive (Rx) port is typically different than the Transmit (Tx) port
  Any device can send to the Rx port
  Controller is typically configured to transmit to a single IP address and port (or has to be configured for each IP you want to send to)

## Slide 11: Questions

## Slide 12: Real World Uses of OSC
Lightwright 6
  Syncs with patch
  Gets cue lists
  Gets groups
iRFR
  Uses OSC as its communication medium
QLab
  OSC has been a great replacement for MSC here – no distance limits, great flexibility for audio/lighting show control

## Slide 13: Real World Uses of OSC: Configurable
TouchOSC
  Simple to very complex configuration
  iOS/Android with desktop config utility
OSCWidgets
  Desktop application – great for troubleshooting and testing!
OSCRouter
  Need to make OSC platform X talk to OSC platform Y?
#lighthack
  Diving into the world of Arduino!

## Slide 14: Real World Uses of OSC - Advanced
Colorsource OSC
  Uses Ethernet to do OSC, based on lighthack
  Not bidirectional
Upcycling a Berkley Colortran analog console
  Low resolution analog sensitivity
  Mapped to Eos faders

## Slide 15: Real World Uses of OSC - Advanced
Color Proximity Sensor
  Uses an inexpensive sensor to get distanance and send HS values to the console
PiBags
  At CUE 2017, we had a bean bag toss game that used optical sensors, Raspberry Pis, microphones, Eos, Sound2Light, and QLab to register points and trigger lighting and sound effects
Python and C++ libraries
  Several code libraries exist that make the process of parsing and using OSC messages easier in your application

## Slide 16: Real World Uses of OSC
danceosc
  Python script to link Eos cue lists together dynamically
  Uses pyosc library https://github.com/ptone/pyosc
  Start with at least two tab-separated value files (TSV)
    The list of acts (each line has Cue List # <tab> Dance name <Tab> Dance description
    The order of acts for a performance (each line has Cue List # <tab> Dance name
  ./fixmyshow.py
    Creates the cue lists in Eos with the number specified
    Copies from a template cue list in the showfile
  ./stitchmyshow.py
    Reads the list of acts and the order for the performance
    Sends OSC to Eos for it to link all the cues together. Just press Go and the entire show executes in order

## Slide 17: Demo: Eos and OSCWidgets
OSCWidgets is a really useful tool that can be used to test OSC commands and diagnose behavior

## Slide 18: Let’s Play
There are workstations set up and a variety of things available
Feel free to try out one of the exercises listed
Ask, explore, enjoy!